## Slide 1: Overcoming Challenges to Certifying Multicore Avionics
Brian Riley <bjriley@ghs.com>

## Slide 2: Agenda
Our Multicore Certification Credentials
AMC 20-193: Use of Multi-Core Processors
Robust Partitioning
Bandwidth Allocation
Cache Partitioning

## Slide 3: Our Key Credential: World’s First Multicore TSOs
PU-3000 Multicore Avionics Computer |  | March 2021 TSO-C198 (AFGCS Equipment) Authorized as a Flight Director
MFD-3068 Multicore Smart Display |  | May 2021 3 Separate TSO Authorizations: TSO-C113, TSO-C165, TSO-C209 Drives up to 4 displays, incl. PFD Multiple apps of mixed criticality
All TSOs included DO-178C DAL A and CAST-32A objectives
Both systems run the INTEGRITY®-178 tuMP™ RTOS
Notes: It wasn’t until late last year that another company got a multicore TSO, and that was 5 years later than they originally claimed would happen.

## Slide 4: AMC 20-193: Use of Multi-Core Processors
Main topic is contention for shared resources
  Memory, cache, on-chip interconnect, and external interfaces
9 Objectives
  Very little change from CAST-32A
New Definition of Integrated Modular Avionics (IMA), which requires
  Robust resource partitioning
  Robust time partitioning
Example Shared Resource Contention:
Attempt to access DRAM while it is in use
X

## Slide 5: Robust Partitioning in AMC 20-193
Multicore Robust Resource Partitioning is Manageable
  Using the memory management unit (MMU) and other well-established techniques
Multicore Robust Time Partitioning is Very Challenging
 Need a way to mitigate all or almost all sources of interference
“No software partition consumes more than its allocation of execution time on the core(s) on which it executes, irrespective of whether partitions are executing on none of the other active cores or on all of the other active cores.”

## Slide 6: Benefits of Meeting IMA Robust Partitioning
Significantly Less Software Verification per AMC 20-193:
Verify software applications separately
Determine their WCETs separately
Results:
Incremental module design and acceptance
Applications are independently modifiable
Platform behavior may be verified independently of specific applications
Operating System or Hypervisor with Robust Partitioning
App 1
App 2
App 3
App 4
App 5
An application can be modified or replaced without testing and reverifying the entire system.

## Slide 7: Achieving Robust Time Partitioning
Allocate and enforce bandwidth from cores to shared resources
  Although some CPUs have a HW implementation, it is immature, complex, and not in CPUs used for avionics
INTEGRITY®-178 tuMP RTOS Implementation
  Bandwidth Allocation and Monitoring (BAM)
Bandwidth Allocation
General Solution: Bandwidth Allocation

## Slide 8: Example: Multicore DRAM Interference
Chart: WCET with Interference
| None | One | Two | Three
Unmitigated | 1 | 7.1 | 13 | 13.6

## Slide 9: Example Bandwidth Allocations
Software architect allocates the shared bandwidth on a per core basis
Max bandwidth is enforced by the RTOS continuously over a very small quantum of time
80%
60%
40%
20%
0%

## Slide 10: Results with BAM in INTEGRITY-178 tuMP
Chart: WCET with BAM Mitigation
| None | One | Two | Three
Unmitigated | 1 | 7.1 | 13 | 13.6
25% Allocation | 4.9 | 4.9 | 5 | 5.4
50% Allocation | 2.4 | 2.4 | 2.8 | 3.4
80% Allocation | 1.4 | 1.4 | 1.6 | 1.7

## Slide 11: Shared Cache Interference is Different
Problem is Inter-Core Cache Line Eviction
  Task on Core 0 goes to read its data, but a task on Core 2 caused new data to be loaded instead
Contention for Access in Not an Issue
Shared Cache Supports Simultaneous Access


## Slide 12: Multiple Memory Locations Map to Same Cache Line/Set
Cache Line
Physical Memory
4-Way Set-Associative Cache
Cache Sets
Challenge: Deconflicting the virtual-to-physical memory mapping so that different cores do not use the same cache line

## Slide 13: Hardware-Based Cache Partitioning to the Rescue!
Cache Line
Physical Memory
Allocate a Cache Way to a Core
Cache Sets
Core 1
Core 2
Core 3
Core 4
Example: Intel® Cache Allocation Technology
* Tasks are assigned to a Class of Service (CLOS)
* Each CLOS is mapped to one or more cache ways

## Slide 14: Overcoming Multicore Certification Challenges
www.free-powerpoint-templates-design.com
01
02
03
04
Goal: Robust Partitioning eases development and verification
Solution:
Bandwidth Allocation mitigates most sources of multicore interference
Cache Partitioning mitigates non-contention interference
Implementation:
INTEGRITY-178 tuMP has both bandwidth allocation and cache partitioning thus enabling robust partitioning